Petition No. 1035

The Connecticut Light and Power Company

Montville Substation

Staff Report

September 6, 2012

On August 7, 2012, the Connecticut Siting Council (Council) received a petition from The Connecticut Light and Power Company (CL&P) for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need is required to modify an existing substation located at 81 Lathrop Road in Montville.  A field review of the petition was conducted on September 4, 2012 by Council member Jerry Murphy, Council staff member Robert Mercier, and CL&P representatives John Morissette, John Nicosia, and Bernard Miller.

CL&P proposes to replace two 345- to 115-kV autotransformers, two 115-kV circuit breakers, and two 345-kV circuit switchers.  The existing equipment is at the end of its service life.

All work would be performed within the existing substation. The new transformer equipment would be installed adjacent to the existing transformer equipment, and once energized, the existing transformer equipment would be removed.  CL&P proposes to begin work in Fall 2012 with completion in December 2013.

CL&P discussed the project with the Town of Montville and no issues were reported.  The autotransformers would be shipped by barge to the Montville Power Station, adjacent to the substation.  Remaining equipment would be shipped via truck.  CL&P would coordinate with the Town to determine a suitable truck route through the Lathrop Road neighborhood.

All work would occur in the west portion of the existing, fenced substation.  The proposed equipment would be similar in appearance and height to that of existing substation equipment.