Petition No. 1053

The Connecticut Light and Power Company

New Canaan, Connecticut

Staff Report

January 24, 2013

On December 6, 2012, the Connecticut Siting Council (Council) received a petition from The Connecticut Light and Power Company (CL&P) for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need is required for the proposed removal of a 30-foot tall wood pole and the installation of an 84-foot steel monopole at a CL&P substation on Lakeville Avenue in New Canaan, Connecticut. Council Chairman Robin Stein and Siting Analyst Robert Mercier visited the site on January 22, 2013 to review the proposal. John Morissette, Steve Florio and Mike Carbary represented CL&P at the field review.

The Lakeville Avenue substation is located at the corner of Lakeview Avenue and New Norwalk Road (Rt. 123) in New Canaan. CL&P currently has two omnidirectional antennas installed at the top of the existing 30-foot tall wood pole located in a fenced storage yard adjacent to the north side of the substation. CL&P is proposing to replace the existing wood pole with an 84-foot Corten steel monopole. A new 14-foot 900 MHz whip antenna would be installed at the top of the new pole. Radio equipment and a 6-hour battery pack would be installed on the tower base.

The purpose of the new pole’s installation is to improve CL&P’s Distribution Supervisory Control and Data Acquisition system, which monitors the operation of CL&P’s electrical distribution system and operates some of the system components (i.e., reclosers) remotely.

The substation storage yard is buffered by deciduous trees along the north and east sides.  The substation is located to the south. A paved roadway serving the Town’s transfer station is located to the west, beyond which is a large cemetery. Views of the new pole would mainly be from an apartment complex to the northwest.

CL&P notified the abutters and the Town.  No comment was received to date.

The proposed tower replacement is not expected to have any substantial adverse environmental effect. The power destiny is calculated to be less than 1% of the FCC’s maximum permissible limit.

Site Location at Lakeview Avenue Substation

View from apartment complex entrance.

# Text boxes

Pole location