Petition No. 361

Connecticut Light & Power

Staff Report

November 21, 1996

On October 28, 1996, the Connecticut Light and Power Company (CL&P) petitioned the Connecticut Siting Council (Council) for a proposed modification to existing transmission line support Structure No. 8600, along the Ludlow, Massachusetts to Meekville Junction 345-kV transmission line in Somers, Connecticut.  CL&P proposes to install steel supports on the top of the structure to allow raising the existing crossarm 4.5 feet higher on the approximately 74-foot high, H-frame structure.  The change in crossarm height would increase the conductor’s ground clearance height at mid-sag, thereby allowing CL&P to operate the line at higher long-term and short-term emergency loads without exceeding clearances over off-road areas, passable by tall vehicles, in accordance with National Electric Safety Code standards.

This proposed change appears to be minor with no significant impact on the environment of the immediate area.  This change is part of CL&P’s continuing plan to upgrade interstate transmission lines in preparation for the importation of transmission capability to alleviate Connecticut generation shortages during peak periods.

Construction would commence and end in the first quarter of 1997.

JMR:TEF:mmb