Petition No. 395

Wilton, Connecticut

Omnipoint Communications Inc.

Staff Report

July 9, 1998

On June 22, 1998, the Connecticut Siting Council (Council) Executive Director, Joel M. Rinebold, Council members Brian Emerick and Ed Wilensky, and Paul Aresta and Robert Erling of the Council Staff met with Sharon Burrows, Kenneth Jenkins, Michael Lund, Steven Lingard and Brian Weinstein of Omnipoint Communications, Inc. (Omnipoint) for a field review on a petition in the Town of Wilton, Connecticut.  Omnipoint is petitioning the Council for a determination that no Certificate of Environmental Compatibility and Public Need (Certificate) would be required for modifications to an existing Connecticut Light and Power (CL&P) electric transmission line facility in Wilton.  Omnipoint submits no Certificate would be required because the addition of the antenna and associated equipment would not have a substantial adverse environmental effect.

Omnipoint proposes to attach one dual pole PCS antenna to existing CL&P transmission line structure number 2997, located off of Old Station Road in Wilton, Connecticut.  Access would be from Wilton Station, a commuter train parking lot.  A temporary 15-foot by 20-foot staging area would be built immediately west of the base of the 90-foot CL&P lattice tower.  All proposed construction would take place within the existing CL&P Right-of-Way (ROW).  The top of the Omnipoint Accelerator antenna would extend to approximately 98 feet 8 inches above ground level (AGL) on the tower.  The proposed antenna is 72 inches in height, 16 inches in diameter, and weighs 150 lbs.  The communications equipment would be installed in an equipment cabinet placed on a 10-foot by 5.5-foot concrete pad located within the legs of the tower.  There are no wetlands at the tower site.  Some existing brush would be trimmed inside the tower base.  The total calculated radio frequency power density at the base of the tower would be 0.0179 mW/cm2, 1.8 percent of the maximum permissible exposure for uncontrolled environments based on Federal Communications Commission (FCC) Bulletin 65, August 1997.