Petition No. 408

United Illuminating Company

Fairfield, Connecticut

Staff Report

December 17, 1998

On December 15, 1998, Connecticut Siting Council (Council) Executive Director, Joel M. Rinebold, Brian Emerick of the Council, and Council staff Robert Erling met Ronald Mongillo of the United Illuminating Company (UI) for a field review of this proposed project in Fairfield, Connecticut.  UI is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) would be required for modification to the Hawthorne Substation in Fairfield.  UI submits no Certificate would be required because the proposed modification would have no substantial adverse environmental effect.

UI proposes to add three current limiters and a new 35-foot transmission line takeoff structure at the substation.  The proposed project would serve to protect the existing number 1222 Old Town to Hawthorne and number 1710 Trumbull Junction B to Old Town transmission lines from potential overloading conditions due to the addition of the Bridgeport Energy Project (Petition No. 377) to the existing electric transmission system.

The proposed height of the new takeoff structure would be the same as existing similar structures.  The height of each current limiter would be approximately 18 feet.  To provide sufficient safety clearances, approximately 75 feet of an existing fence line would be moved out 10 feet.  Six trees would be removed along the fence line to accommodate the new fence location.  UI expects the project to take two to three months to complete, with all work taking place during daytime hours.  UI proposes to plant white pines along the southern fence line to provide screening for two residences nearby.  No wetlands would be impacted by the project.