# Petition No. 410

# Hull Forest Products, Inc.

# Staff Report

# March 24, 1999

On March 18, 1999, Connecticut Siting Council (Council) members William H. Smith and Gerald J. Heffernan, and Council staff Joel M. Rinebold and Paul M. Aresta met Hull Forest Products, Inc. (HFP) representatives Lawrence J. Golden and Jeffrey M. Durst for a site inspection of two electric generators located at the HFP facility, 101 Hampton Road in Pomfret, Connecticut.  HFP is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the placement and operation of two diesel generators at the HFP facility.

HFP replaced two 13 year old backup diesel generators totaling approximately 640 kW with two new diesel generators to self-generate electricity at its existing sawmill plant.  The larger 1,000 kW generator will run during first shift production hours, while the smaller 200 kW generator will run at other times.  The new generators were placed within the existing building that was used for the two backup generators, and will be serviced by an existing 10,000 gallon above-ground fuel tank with secondary containment, which was installed in 1997.  Electricity produced by the two generators would not be supplied to the regional electric system (grid).

The HFP facility is located on approximately 15 acres and consists of a total of 11 buildings.  The surrounding land uses include forest land and agricultural cropland.  There are no wetlands within 430 feet of the facility.  The nearest residence, other than the petitioner’s residence, is located approximately 1,800 feet away from the existing generator building.

HFP has applied to the Department of Environmental Protection Bureau of Air Management for a stationary source permit.  The nitrogen oxide (NOx) emissions from the facility would be 39 tons per year.  HFP contends that the placement of two generators totaling 1,200 kW at its existing sawmill facility would not impact nearby residences or wetlands; would not be a major source of air emissions; would have no water-related impacts; and would not cause a substantial adverse environmental effect.