Petition No. 411

Springwich Cellular Limited Partnership

Stratford, Connecticut

Staff Report

March 24, 1999

On March 22, 1999, Daniel P. Lynch, Jr., of the Connecticut Siting Council (Council) and Robert K. Erling of the Council staff met Marshall West of Springwich Cellular Limited Partnership (Springwich) for a field review of this petition in Stratford, Connecticut.  Springwich is petitioning the Council for a determination that no Certificate of Environmental Compatibility and Public Need (Certificate) would be required for modifications to existing Connecticut Light and Power (CL&P) electric transmission line # 1570 and structure # 1322 off of Harvest Ridge Road in Stratford.

Springwich submits no Certificate would be required because the installation of its antennas and associated equipment at this tower would not have a substantial adverse environmental effect.

Springwich proposes to attach its panel antennas to the top of the existing 82-foot CL&P electric transmission line lattice tower.  The top of the antenna would be approximately 99.4 feet above ground level.  At CL&P’s request the antenna platform would be designed to support Springwich’s antennas only.  Other nearby transmission towers range from 90 to 95 feet in height.

Springwich would install a 12-foot by 26 foot equipment shelter within the transmission line right-of-way near the base of the tower.  An eight-foot security fence would be placed around the equipment shelter.

Access to the transmission line tower would be from Harvest Ridge Road onto land currently owned or covered by the right-of-way agreement held by CL&P.  This approximately 150-foot permanent driveway would be constructed to access the tower both during antenna installation and during maintenance.

The area surrounding the transmission line structure includes residential lots.  This site is bordered by an unoccupied CL&P-owned residential lot to the south.  The nearest home is approximately180 feet to the north; two other homes across Harvest Ridge Road would also have an unobstructed view of the antenna post used to hold the Springwich antennas.

There are no wetlands in the vicinity of the tower site.  All erosion and sediment control measures would be installed as required in accordance with the Connecticut Guidelines for Soil Erosion and Sediment Control.

The total calculated radio frequency power density at the base of the tower would be 0.0835 mW/cm2, 14.24 percent of the maximum permissible exposure for uncontrolled environments based on Federal Communications Commission Bulletin 65, August 1997.