Petition No. 427

Aetna Life Insurance Company

Hartford, Connecticut

Staff Report

August 31, 1999

On August 24, 1999, Connecticut Siting Council (Council) member Daniel Lynch, Jr. and Council staff Fred Cunliffe, met Aetna Life Insurance Company (Aetna)  representative Michael Marshall for a site inspection of the proposed installation of emergency generating devices at 151 Farmington Avenue, Hartford.  Aetna is petitioning for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the installation of these emergency generating devices.

Aetna proposes to install four 2.0 megawatt diesel-fueled emergency generating devices at their Hartford offices. This proposal is consistent with the Middletown and Windsor installations and prepares Aetna for Y2K readiness. The proposed site is an existing paved parking area surrounded by the main office building to the north, a mechanical building containing refrigerant chillers, cooling towers, water pumps and related equipment to the east, an Amtrak rail line, parking lot, and an elevated portion of I-84 to the south, and a five-story parking garage to the west.

The proposed facility and operating characteristics are as follows:

| Facility | 151 Farmington Avenue, Hartford |
| --- | --- |
| Quantity and Capacity | (5) Five - 2 megawatt generators |
| Maximum Operation | 297 hours per generator |
| % Annual Availability | 3.3% |
| Maximum Fuel Consumption | 41,246 gallons / generator / yr. |
| Fuel Storage | 2,000g above-ground double wall tank |
| Area of Addition/Site Area | .01 acre / 22 acres <1% |
| Unit Dimensions = L x W x H | 48 ft x 8.6 ft x 12 ft |

Aetna proposes to submit a General Permit to Construct and/or Operate a New or Existing Emergency Engine to the Department of Environmental Protection. One or more generators will operate simultaneously, dependent on the actual load during an emergency.

Aetna contends that each of the proposed emergency generating devices has a capacity of less than five megawatts; the generators would be installed for the purpose of producing emergency back-up electrical power; operation will be limited to less than 500 hundred hours per year for each unit; Aetna is not an entity which is an electric or gas company. Aetna further contends that the generating devices will not have a substantial adverse environmental effect, and are emergency generating devices as defined in CGS Sec. 16-50i (f) and are therefore except from Council jurisdiction.

On December 13, 1989, the Council ruled that the installation of four 1.25 megawatt (MW) generating devices at Aetna’s Windsor office at 570 Pigeon Hill Road would not require a Certificate (Petition No. 241).  Similarly on July 15, 1997, the Council ruled that the replacement of six 1.0 MW emergency generating devices with five 2.0 megawatt emergency generating devices at Aetna’s Middletown offices and installation of six 1.0 MW emergency generating devices at its Windsor offices would not require a Certificate (Petition No. 378).