Petition No. 436

Docket 177A

Crown Atlantic Company LLC

Staff Report

October 21, 1999

On October 20, 1999, Connecticut Siting Council (Council) member William H. Smith, Ph.D., and Council staff Steve Levine met Jennifer Young Gaudet of Pinnacle Site Development (representing AT&T) to conduct a field review of Crown Atlantic Company’s (Crown) Ogg Meadow Road telecommunications tower in Orange.  Crown proposes to modify the tower to permit use by AT&T, and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.  Crown submits that the proposed modification will not have a substantial adverse environmental effect, but instead will reduce the unnecessary proliferation of telecommunications towers by utilizing an existing structure, and qualifies for an order of tower sharing pursuant to C.G.S. § 16-50aa.

The Ogg Meadow Road tower is a 160-foot-tall monopole tower.  In 1997, the Council approved a maximum height of 160 feet above grade, excluding antennas, in Docket 177A.  The tower presently supports antennas owned by Bell Atlantic Mobile, Springwich Cellular, Nextel, and Sprint.  An engineering study submitted by Crown indicates the tower is capable of supporting all of these antennas and the proposed AT&T antennas as well.

AT&T would install three panel-type antennas to a 4.5-inch diameter heavy-duty pipe mounted at the 160-foot top of the existing tower (7’ 10” of pipe would be visible below the 4’ 8”-high antennas).  The antenna cluster itself would have a diameter of approximately 35”.  The AT&T antennas would extend to a total height of 172.5 feet above grade.  AT&T also plans to install a new 12 x 20-foot equipment building within existing fencing at the base of the tower.

Crown argues that the height of the tower itself will remain 160 feet, notwithstanding addition of the antennas.  Crown cites specific language contained in the Decision and Order for Docket 177A, which excludes antennas from the height determination.

The proposed antennas and associated equipment will not increase the noise levels at the existing site, under normal operating conditions, by six decibels or more.  The worst case power density for the telecommunications operations at the site has been calculated to be 20.3% of the applicable standard for uncontrolled environments, including a contribution of 1.0% by AT&T.  Crown asserts that the proposed installation will not cause a substantial adverse environmental effect, and for this reason would not require a Certificate.