Petition No. 456

Voicestream Wireless

Redding, Connecticut

Staff Report

May 10, 2000

On May 4, 2000, Connecticut Siting Council (Council) member Gerald J. Heffernan, and Fred Cunliffe of Council staff met Voicestream Wireless (Voicestream) representatives J. Brendan Sharkey, Esq., Chetan Dharduk, and Brian Raggozine for inspection of a Connecticut Light & Power Company (CL&P) electric transmission line structure (no. 3261) located off Peaceable Street in Redding.  Voicestream, with the agreement of CL&P, proposes to modify the transmission structure for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

Voicestream proposes to attach an 4.5-inch diameter pipe extending the existing monopole height of 70 feet by 19 feet for a total height of 89 feet.  A structural analysis concludes no additional reinforcement is necessary.  Voicestream proposes to install two low profile antenna cluster mounts with centers of radiation at 85 feet and 78 feet 4 inches on the pipe and placing associated equipment cabinets on a concrete foundation within a 10-foot by 10-foot compound secured by a six-foot chain link fence. Utilities would be placed overhead 40 feet from a distribution pole on Peaceable Street tyo a new pole on the edge of the right-of-way and placed 70 feet underground to the site.

The proposed site is within a CL&P easement within a rural setting with a CL&P substation south across the street from the proposed structure.  The nearest home is approximately 250 southwest of the site. Buffers of vegetation exist on both sides of the right-of-way.

The worst case power density for the telecommunications operations at the site has been calculated to be less than 5.6% of the applicable standard for uncontrolled environments.

Voicestream that the proposed installation will not cause a substantial adverse environmental effect, and for this reason would not require a Certificate.