Petition No. 467

AT&T Wireless PCS, Inc.

Greenwich, Connecticut

Staff Report

June 20, 2000

On June 16, 2000, Connecticut Siting Council (Council) member Edward S. Wilensky, and Fred Cunliffe of Council staff met AT&T Wireless PCS (AT&T) representatives Michael Austin, Carmen Chapman, and Lisa Hazen for inspection of a Connecticut Light & Power Company (CL&P) electric transmission line structure (no. 1255) located off Sound Beach Avenue at the Old Greenwich Railroad Station.  AT&T, with the agreement of CL&P, proposes to modify the transmission structure for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

AT&T proposes to attach a 14-inch diameter by 10-foot high mast to an existing 95-foot tall monopole electric transmission structure.  A total of six, four-foot high panel antennas, in a triangular layout, would extend out four feet from the top of the tower.  The total height of the structure with antennas would be 107 feet.  A structural analysis concludes no additional reinforcement is necessary for this proposal.  Also, AT&T has an agreement with the Connecticut Department of Transportation to construct a 12-foot by 20-foot equipment building adjacent to the base of the existing CL&P structure.  Clearing of vegetation is necessary and Council staff recommends that no trees be cleared beyond 25 feet of CL&P’s structure.  AT&T proposes to plant trees west of the building providing screening to the railroad station parking lot.  The proposed site is south of the Old Greenwich Railroad Station and east of a golf course. A fence with vegetation borders the golf course, which would not be disturbed.

An existing parking lot off Sound Beach Avenue would be used by AT&T to access the structure. Utilities would be routed underground approximately 30 feet from an existing utility distribution pole to the site.

The worst case power density for the telecommunications operations at the site has been calculated to be less than 3% of the applicable standard for uncontrolled environments.

AT&T contends that the proposed installation will not cause a substantial adverse environmental effect, and for this reason would not require a Certificate.