Petition No. 468 and Docket No. 184

AT&T Wireless Services

New Hartford, Connecticut

Development and Management Plan

August 10, 2000

On July 27, 2000, AT&T Wireless Services (AT&T) submitted a request that the Connecticut Siting Council (Council) reconsider a declaratory ruling that no amendment to the Certificate of Environmental Compatibility and Public Need, issued by the Council in Docket No. 184 on June 25, 1998, would be required to allow relocation and expansion of the leased parcel and a relocation of the access road.  This filing included a revised Development and Management Plan (D&M Plan) for the New Hartford tower site. The facility to be developed is located within a 2.3-acre parcel of property owned by the South End Fire District (SEFD).

In order to accommodate future co-location of telecommunications carriers, AT&T has increased its leased parcel size from 50 feet by 50 feet to 75 feet by 75 feet.  To accommodate the increase in leased parcel size and minimize impact to a slope north of the site, AT&T would shift the center location of the leased parcel approximately 55 feet further south including the access road. However, development of the site would comprise of a 50- by 50-foot compound, which complies the Council’s Decision and Order.

The D&M plan includes plans for a 115-foot monopole tower.  The SEFD would mount a 16-foot whip antenna to the top of the tower followed by Nextel Communications of Mid-Atlantic, Inc. (Nextel) attaching three whip antennas at the 95-foot level of the tower with a centerline radiation at 101 feet, AT&T attaching a twelve-foot wide antenna platform supporting 12 panel antennas with a centerline radiation at 90 feet, and Springwich Cellular Limited Partnership (Springwich) attaching a twelve-foot wide antenna platform supporting 12 panel antennas with a centerline radiation at 84 feet.  To accommodate future co-location, the tower and its foundation have been designed to accommodate up to a total of six wireless carriers, with extension of up to 145 feet, if approved by the Council.  The base of the monopole would be approximately 5 feet in width tapering to approximately 3 feet in width.  The tower would be placed on a 7.5-foot square pedestal on a 27.5-foot square by 4-foot thick concrete foundation.  The Federal Aviation Administration does not require lighting or marking for the proposed 115-foot tower.

One 12-foot by 26-foot equipment building for AT&T, one 11.5-foot by 20-foot equipment building for Springwich, one 10-foot by 20-foot equipment building for Nextel, and a 6-foot by 12-foot equipment building for the SEFD would be installed.  These buildings would not be architecturally treated, however, an eight-foot high wood fence of shadow box design would enclose the 50-foot by 50-foot leased compound. The site is within an area of trees which provide some buffer to a school located approximately 265 feet to the south.

A new 110-foot gravel covered access drive with a turn around area would be constructed from Antolini Road to the site. Electric and telephone utilities would be placed overhead 80 feet to cross Antolini Road and then placed underground within the access drive with the transformer located near the turn around area. Erosion and sediment controls would be placed on the north side of the site and new access drive, including an anti-tracking pad on the access road leading to the site.  A temporary refueling containment area would be installed adjacent to the west side of the site.

AT&T conducted an archeological reconnaissance survey for the new leased parcel.  No artifacts or other evidence of archeological sites were discovered for either the 1997 or 2000 survey of the project sites.

Since no landscaping plan nor power density analysis was provided, Council staff recommends that the site be flagged and inspected by Council staff prior to clearing, landscaping be reviewed after construction, and a power density analysis for the facility be provided prior to the commencement of operation.

AT&T has notified the Council of its intent to begin access work and construction of the facility immediately after approval of the Development and Management Plan.

AT&T contends that the proposed expansion of the leased parcel, and relocation of the compound area and access road does not require an amendment to a Certificate of Environmental Compatibility and Public Need.