Petition No. 477HW

United Oil Recovery, Inc.

Meriden, Connecticut

Staff Report

September 19, 2000

On September 13, 2000, Connecticut Siting Council members William H. Smith and Daniel P. Lynch, Jr., and Fred Cunliffe and Christina Lepage of Council staff met with William Morris, Rick Baker, Brian Avery, and David Carabetta of United Oil Recovery, Inc. at its facility located on 136 Gracey Avenue, Meriden. United Oil Recovery seeks a declaratory ruling from the Council that the proposed modifications to install a container washing station and one bay door to Bay 4 of the liquid recycling facility would not require a Certificate of Public Safety and Necessity.

United Oil Recovery uses Bay 4 of the liquid recycling facility to receive containerized waste. Presently, one door services this bay (12 feet by 60 feet in area) which requires United Oil Recovery to shift containers two or more times. United Oil Recovery seeks to improve access to the containers by adding another bay door to the west side of the building.  This would allow United Oil Recovery to handle containers with less movement.  The new bay door would face Duffy Avenue, a dead end road in an area zoned Commercial/Industrial.

United Oil Recovery also plans to install a container wash station in a 7-foot by 12-foot area of Bay 4.  Currently, containers are pumped to a truck which is unloaded in another bay to a degrit tank.  The container wash station would be connected via a discharge line that leads to the degrit tank, removing the need for a pump truck. Venting for the wash station would be tied into an existing vapor recovery system.

No addition to the size of the bay is proposed.  Furthermore, the epoxy floor in Bay 4 with closed bay doors meets RCRA secondary containment.  When the bay doors are open spill management materials and on-site catch basins would contain a spill.

The City of Meriden has been informed of this petition and has issued a building permit for the proposed bay door.

United Oil Recovery contends the proposed refinements would mean less movement of waste and, therefore, a more efficient, safe, and environmentally sound operation; are not significant changes; and would not require a Certificate from the Council.