Petition No. 493

VoiceStream Wireless

Brookfield, Connecticut

Staff Report

December 14, 2000

On November 20, 2000, Connecticut Siting Council (Council) member Edward Wilensky and Christina Lepage of the Council staff met with VoiceStream Wireless (VoiceStream) representative Brendan Sharkey off of Vale Road, Brookfield, Connecticut for inspection of an electric transmission structure. The property and structure is owned by Connecticut Light and Power Co. (CL&P).  VoiceStream Wireless, with the agreement of CL&P, proposes to modify the structure by installing antennas and associated equipment for telecommunications use and is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for the modification.

VoiceStream proposes the installation of six EMS dual-pol antennas on top of a 3-inch wide pipe mast extension.  The antennas will extend approximately 17-feet 4-inches above the existing 115-foot transmission line monopole structure (#10247).  The height at the top of the upper set of antennas will be about 132-feet 4-inches above ground level (AGL); the top of the lower set of antennas will be at 125-feet 8-inches AGL.  This design requires a minimum of six feet above the CL&P shield wire and at least two feet in between the antennas.

Two Nortel S8000 equipment cabinets will be mounted on a 13’x12’ concrete slab in a 17’x16’ fenced compound at the base of the tower.  The equipment cabinets do not require any protective structures or air conditioning; therefore no audible noise will be created.  An underground conduit from an adjacent utility pole will provide power to the site, and a microwave will provide telephone service.

The proposed site is located east of Route 7, bordering a railroad and an industrial park in Brookfield.  The zoning designation of this site is IG-80 Industrial.  VoiceStream states that the land use in the surrounding area consists of an office industrial park, a railroad right-of-way and what appears to be a former quarry area.

The worst-case power density for the telecommunications operations at the site has been calculated to be 2.24% of the applicable standard for uncontrolled environments.

VoiceStream contends that the increase in height of this monopole structure will not result in a substantial environmental effect and the proposed project will prevent the construction of a new tower in the area.  VoiceStream also states that the PCS antennas will blend in with the existing transmission line structure, and the placement of the equipment cabinets, which will be directly underneath the existing tower, will limit the disturbance created by construction activities.

VoiceStream submits that the proposed modification of the structure would not require a Certificate because it will reduce the need for a new telecommunications tower by utilizing an existing structure and contends that the proposed installation will not cause a substantial adverse environmental effect.