Petition 496

Remote Meter Reading Project - Cell Master Units

The United Illuminating Company

Staff Report

December 14, 2000

On December 7, 2000, Connecticut Siting Council (Council) member Gerald J. Heffernan and Council staff Paul M. Aresta met United Illuminating Company (UI) representatives John Walter, Brian M. Horgan, and Bohdan Katreczko for field reviews of this petition.  UI is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need would be required for the placement of antennas and associated equipment at seven locations within UI’s service area as part of a remote meter reading network.

UI proposes to install seven Cell Master Units (CMU), each consisting of an approximately ten-foot high by three-inch diameter antenna and base station equipment, at various locations within its service area.  Each proposed CMU would serve as a regional data collector for receiving transmitted metering information from micro cell controllers (MCCs), and then forward the metering data via land line to UI’s corporate headquarters.  Each proposed CMU would transmit a signal to the MCCs it serves while operating at a maximum of five watts on one channel at a height approximately 79 feet above ground level for a predicted maximum electromagnetic power density of 0.046 percent of the applicable ANSI standard for the general population.  The cumulative maximum electromagnetic power density for the North Haven tower would be 9.12 percent of the applicable ANSI standard.

The proposed base station equipment cabinet would be approximately 49 inches high by 44 inches wide by 20 inches deep.  The equipment cabinets would be mounted directly to the wood pole structures, approximately two feet above the ground, while the base station equipment cabinets for the transmission line support structure and the telecommunications towers would be on a stand on the concrete pad at each facility.

| Location | Existing Structure | Proposed Structure | Land Use |
| --- | --- | --- | --- |
| Wesley Heights Road, Shelton | 40-foot Distribution Pole | 79-foot Distribution Pole | High Density Residential |
| Mohegan Road Drive, Shelton | None | 79-foot Pole | Town Recreation Area |
| Bob White Lane, Trumbull | Transmission Structure | Transmission Structure | Residential |
| Stemway Road Ext., Trumbull | None | 79-foot Lighting Pole | Residential/School |
| Talmadge Road, Hamden | 40-foot Distribution Pole | 79-foot Pole | Rural |
| Washington Ave, North Haven | Telecomm. Monopole | Telecomm. Monopole | Commercial |
| Totoket Rd/Rt. 80, No. Branford | Telecomm. Monopole | Telecomm. Monopole | Rural |

UI has contacted each of the towns of the proposed installations.  UI contends that the proposed project uses existing structures and areas within rights-of-way or easements to the extent possible, minimizing the visual impact; and no wetlands would be impacted nor would any vegetation be removed or cleared