Petition No. 503

Connecticut Light & Power Company

Staff Report

April 12, 2001

On April 10, 2001, Connecticut Siting Council (Council) member Brian Emerick and Christina Lepage of the Council staff met with Connecticut Light and Power Company (CL&P) representative Mike Carlson and Frank Woodhouse to review proposed modifications to the Montville - Dudley – Bean Hill transmission line in Montville, Connecticut.  CL&P is petitioning the Council for a declaratory ruling that the proposed project would have no substantial adverse environmental effect.

The Council approved Petition No. 248 on April 10, 1990, which allowed for the resagging of the entire circuit to increase the capacity of the line.  During final engineering, NU was informed by the CT Department of Environmental Protection that the actual mean water level of Horton Cove is five feet lower than originally identified.  As a result, the transmission line span over the Cove was re-rated to a higher ampacity without a need to resag this section of the line.  This existing ampacity is no longer adequate to support increased system load.  CL&P now proposes to resag this section of the line as a measure to increase the capacity of the circuit.

The proposed project includes resagging the southeasterly phase conductors by increasing the conductor tension.  Structural reinforcement will be necessary because of the increased tension.  An 8’x8’ concrete slab will be used to anchor to the existing foundation and rock ledge of two legs of tower #7607, which is located on the western side of Horton Cove.  An 18’x18’ concrete slab will be used to anchor the existing foundation and rock ledge of two legs of tower #7608, which is located on the eastern side of Horton Cove.  Construction would include E&S controls to minimize erosion and control sedimentation to Horton Cove.

Construction would be completed by June 1, 2001.

JMR/CML