# Petition 504

Remote Meter Reading Project - Cell Master Units

# The United Illuminating Company

# Staff Report

# August 8, 2001

On July 20, 2001, Connecticut Siting Council (Council) member Gerald J. Heffernan and Council staff Paul M. Aresta met United Illuminating Company (UI) representatives Brian M. Horgan and Bohdan Katreczko for field reviews at Mohegan Road, in Shelton.  UI is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need would be required for the placement of an antenna and associated equipment on a 79-foot distribution pole at Mohegan Road in Shelton.

On April 12, 2001, the Council approved the placement of a Cell Master Unit (CMU), consisting of an approximately ten-foot high by three-inch diameter antenna and base station equipment on a 79-foot wood pole on Mohegan Road Drive, in Shelton.  The Shelton Board of Alderman denied UI's request to modify the easement for the placement of the proposed CMU on Mohegan Road Drive.  Consequently, UI proposes to replace an existing approximately 40-foot tall distribution pole (UI pole #3484) with a new 79-foot tall wooden pole on Mohegan Road.  The new site is located approximately 40 feet west of the intersection of Mohegan Road Drive and Mohegan Road, in Shelton.

An Ad-Hoc Committee of concerned citizens in the Town of Shelton has been formed to investigate and make recommendations to the Shelton Board of Alderman regarding the installation of the proposed CMU.

Each proposed CMU would serve as a regional data collector for receiving transmitted metering information from micro cell controllers (MCCs), and then forward the metering data via land line to UI’s corporate headquarters.  The proposed base station equipment cabinet would be approximately 49 inches high by 44 inches wide by 20 inches deep, and would be mounted directly to the 79-foot wood pole approximately two feet above the ground.

The proposed CMU at Mohegan Road in Shelton would transmit a signal to the MCCs it serves while operating at a maximum of five watts on one channel at a height approximately 79 feet above ground level for a predicted maximum electromagnetic power density of 0.046 percent of the applicable ANSI standard for the general population.

UI contends that the proposed project would be within an existing right-of-way, would not impact or disturb any designated wetlands, nor would any vegetation be removed or cleared.