Petition No. 507

Connecticut Light and Power Company (CL&P)

Brookfield, Connecticut

Staff Report

May 10, 2001

On April 27, 2001, Connecticut Siting Council (Council) member Colin C. Tait and Council staff Paul M. Aresta met CL&P representative Robert J. Charpentier for an inspection of the Stony Hill Substation located on Stony Hill Road, in Brookfield, Connecticut.  CL&P is petitioning the Council for a declaratory ruling that the proposed upgrade of equipment at the existing Stony Hill Substation would not have a substantial adverse environmental effect.

CL&P proposes to install a new 115-kV, 25.2-MVAR capacitor bank, a 115-kV circuit breaker, one set of 115-kV current limiting reactors, and a 115-kV disconnect switch.  The proposed equipment would be approximately 21 feet high, and occupy an area approximately 90 feet long by 40 feet wide.  The proposed equipment is required to improve area transmission voltage levels during contingency conditions.  The proposed equipment would be located within the fenced compound of the existing electric substation site.  The proposed work would begin in September 2001, and be completed by April 2002.

The proposed equipment would not be located within wetlands or waterways, the 100-year flood zone, or any stream encroachment lines.  No vegetation would be removed.  CL&P contends that the proposed equipment upgrades would have no visual impact; would not cause interference for television or radio; and would not adversely affect the environment, scenic, historic, and recreational resources.