Petition No. 508

Connecticut Light and Power Company (CL&P)

New Milford, Connecticut

Staff Report

May 10, 2001

On April 27, 2001, Connecticut Siting Council (Council) member Colin C. Tait and Council staff Paul M. Aresta met CL&P representatives Robert J. Charpentier for an inspection of the Rocky River Substation located off of Route 7, in New Milford, Connecticut.  CL&P is petitioning the Council for a declaratory ruling that the proposed upgrade of equipment at the existing Rocky River Substation would not have a substantial adverse environmental effect.

CL&P proposes to install a new 115-kV, 25.2-MVAR capacitor bank, a 115-kV circuit breaker, and one set of 115-kV current limiting reactors.  The proposed equipment would be approximately 21 feet high, and occupy an area approximately 45 feet long by 35 feet wide.  The proposed equipment is required to improve area transmission voltage levels during contingency conditions.  The proposed equipment would be located immediately west of the existing substation equipment within the fenced compound of the existing electric substation site.  The proposed work would begin in September 2001, and be completed by April 2002.

The proposed equipment would not be located within wetlands or waterways, the 100-year flood zone, or any stream encroachment lines.  No vegetation would be removed.  CL&P contends that the proposed equipment upgrades would have no visual impact; would not cause interference for television or radio; and would not adversely affect the environment, scenic, historic, and recreational resources.