Petition No. 563

Amendment

The Torrington Company

Installation of two microturbine generators

Staff Report

October 23, 2002

On June 25, 2002, the Council considered and ruled that the proposed installation of two 70 kilowatt (kw) microturbine generators at the Torrington Company facility would not have a substantial adverse environmental effect, and pursuant to General Statutes § 16-50k would not require a Certificate of Environmental Compatibility and Public Need.

The Torrington Company proposes to install two 70 kW microturbine generators at its Bearing Test building. Each unit measures approximately 43 inches wide by 72 inches long and 87 inches high.  Originally, one microturbine was to be installed within the Bearing Test building and the other microturbine would be installed on the west outside wall of the Bearing Test building.  The Torrington Company has determined that these locations would require a substantial financial burden of the project.

The Torrington Company is requesting an amendment to the initial Council ruling by proposing to install both micoturbines within a new 15-foot by 18-foot enclosure on the north side of the building facing Forest Street.  This enclosure would be architecturally treated to blend in with the existing building.

The microturbines would be fueled by natural gas.  No water is needed for operating the microturbines. No air emission permits are needed because of the very low emission output, which are below the Department of Environmental Protection air emission permit thresholds.  The noise level would be approximately 78 decibels at one meter from the microturbines.  Because the microturbines would be inside the bearing test building and outside in an enclosure, noise impacts would be minimal.

Adjacent land uses include other Torrington Company buildings and parking lots.  The nearest residences to the proposed project are located east across Field Street of the bearings test building, a distance of approximately 150 feet.

The Torrington Company contends that the revised location for installation of the two microturbines would not adversely affect the environment or ecology and has no impact on scenic, historic, or recreational values; and therefore, would not require a Certificate.