Petition No. 578

SBA Properties Inc.

Lebanon, Connecticut

Staff Report

September 5, 2002

On August 8, 2002, Connecticut Siting Council staff conducted an inspection of an existing 156-foot stealth monopole owned and operated by SBA Properties Inc. (SBA) and located at 859 Goshen Hill Road in Lebanon, Connecticut.  SBA seeks a declaratory ruling from the Council that no Certificate of Environmental Compatibility and Public Need (Certificate) is required this existing telecommunications facility.  SBA also requests that the Council approve the proposed shared use of this facility by AT&T Wireless PCS, LLC (AT&T).

This petition was filed in response to the Council’s letter to municipalities dated January 25, 2002.  The letter requested that the owners of speculation and PCS towers which received municipal approval in the period between July 10 and December 17, 2001 submit a petition to the Council for a declaratory ruling as to whether such towers have a substantial adverse environmental effect.  The Lebanon Planning and Zoning commission approved the construction of the tower on November 14, 2001.  Site clearing commenced on November 15.

The existing facility consists of a 156-foot flag monopole located within a fenced, graveled compound.  The tower is designed for to support five levels of antennas.  No carriers are currently located at the facility.  The facility is located on a wooded parcel used as a chicken farm in a rural area.

AT&T proposes to install six panel antennas at the 130-foot level and install two equipment cabinets on a concrete pad at the base of the tower.  A structural analysis report indicates the tower can accommodate the proposed antenna loading.

The calculated worst-case radio frequency (RF) power density level for proposed telecommunications operations at the site would be approximately 6.4% of the applicable American National Standards Institute standard for exposure to uncontrolled environments.

SBA contends that the existing tower and proposed-shared use of the tower and associated compound would not cause a substantial adverse environmental effect, and therefore, a certificate to operate this facility would not be required.