Petition No. 579

Cordless Data Transfer

Norwich, Connecticut

Staff Report

September 5, 2002

On August 27, 2002, Connecticut Siting Council member Gerald Heffernan and staff Robert Mercier conducted an inspection of an existing 140-foot lattice tower owned and operated by Cordless Data Transfer and located at 2 Hinckley Hill Road in Norwich, Connecticut.  T-Mobile is petitioning the Council for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need (Certificate) is required for a proposed 10- foot tower extension.

T-Mobile proposes to install twelve panel antennas at the top of the proposed 10-foot extension.  The total height of the structure would be 153 feet above ground level including antennas.  Three cabinets would be placed within the existing compound.  Locating antennas at the 150-foot level will provide T-Mobile with adequate coverage on Route 12 and would allow call handoff to an existing facility at the Preston Town Hall.

The proposed site is located on a wooded ridge and is screened from surrounding residential areas by existing vegetation.

A structural analysis of the existing 140-foot tower performed by a professional engineer from Fred A. Nudd Corporation indicates that the tower and foundation can support the proposed modifications.  The worst-case power density for the telecommunications operations at the site has been calculated to be 3.7% of the applicable standard for uncontrolled environments.

T-Mobile contends that the proposed extension of the structure would not cause a substantial adverse environmental effect, and therefore, a certificate would not be required.