Petition No. 632E

The Connecticut Light and Power Company

Modifications to 345-kV lines

# Middlefield, Connecticut

August 26, 2003

On June 27, 2003, Connecticut Siting Council (Council) member Philip T. Ashton and Christina Lepage of the Council staff met representatives of the Connecticut Light and Power Company (CL&P) off of Coleman Road, Middletown, Connecticut and continued to Route 66, Middlefield, Connecticut for a field review of this petition.  CL&P is petitioning the Council that its proposed modifications to existing 345-kV line #348 and line #387, would have no substantial adverse environmental effect.

On July 8, 2003, the Council approved the Middletown portion of the proposed project.  At that time, the Middlefield portion of the proposal was tabled until CL&P could provide the Council with a site plan for the removal of the existing lattice structure and installation of two single circuit monopole structures.  On August 11, 2003, CL&P submitted a plan for the existing transmission line structure to be replaced with two single circuit steel poles.  All construction activities would take place within the existing CL&P right-of-way and the new structures would not exceed the height of the existing structure.

Access to the site would be via the Connecticut Department of Transportation right-of-way off of Route 66.  Construction is proposed to take place between November, 2003 and February 7, 2004.  The proposed elimination of the double circuit tower failure contingency for the two 345-kV transmission lines would remove unnecessary operator burden and transmission uplift, improving the reliability of the transmission lines.

CL&P submits that this modification would not result in a substantial adverse environmental effect, nor would it damage existing scenic, historical, or recreational values.