Petition 642: Stafford

T-Mobile

Staff Report

August 26, 2003

On August 21, 2003, Council member Dan Lynch and staff member David Martin met with T-Mobile representatives Stephen Humes, Scott Chassé, and Syer Hassan at an existing tower site on Brendan Street in Stafford Springs. At this site, there is an existing 115-foot tall monopole owned by Crown Castle to which T-Mobile is seeking to add a ten-foot pipe mast extension. This extension would bring the overall height of the tower to 125 feet. T-Mobile would attach three flush-mounted antennas to the proposed extension. T-Mobile’s ground equipment would consist of three cabinets and one power/telco cabinet that would be mounted on concrete slabs within the existing compound.

Streets leading to the site go through a residential neighborhood of middle-class single and multi-family homes. However, the site is set far back in a wooded area with access over a long gravel road. There is one home visible through the trees from the tower compound. But otherwise the site is not visible from the closest residential streets.

A structural analysis has been performed and indicates that the tower can safely support the proposed extension and antennas. T-Mobile’s antennas would add 4.38% of the regulatory power density limit. Council records indicate that this addition would bring the power density of all antenna systems on the tower to 48% of the regulatory limit.

Based on conditions observed during the field review, it is unlikely that T-Mobile’s proposed changes to this facility would cause any significant environmental impacts.