PETITION NO. 705

The United Illuminating Company

Milvon Substation, Milford, Connecticut

March 15, 2005

~~~

On February 16, 2005, The United Illuminating Company (UI) submitted a petition to the Connecticut Siting Council (Council) for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need would be required for proposed modifications to the existing Milvon Substation at 770 Bridgeport Avenue in Milford, Connecticut.  On March 9, 2005, Council member Brian O’Neill and Robert Mercier of Council staff met with UI representatives Eugene Kallaur, Bohdan Katreczko, and Mark Mushkin at the site to review this petition.

UI proposes to replace two 115/13.8 kV bulk substation transformers at the site, specifically the replacement of two 30/40/50 megavolt-ampere (MVA) rated fixed tap transformers with two 36/48/60 MVA-rated automatic load tap changing transformers.  Foundations with oil containment would be installed for the new transformers.  In addition, a dead end structure consisting of two 45-foot steel poles, would be installed at each transformer.

The new transformer and associated dead-end structure installation would occur on the north side of the existing substation building.  The existing transformers scheduled for removal are on the south side of the substation building.  The new transformers would be approximately 24 feet from the south fence of the substation.

The design and location of the new transformers would necessitate the installation of two 70-foot steel poles between the existing substation building and the existing 115 kV bus.  Seventy-foot towers already exist to the rear of the substation to support the 115-kV bus servicing the substation.

The existing fenced substation is surrounded by commercial development and is adjacent to an active railroad right of way owned by the Connecticut Department of Transportation.  No expansion of the substation is proposed.