Petition No. 865

The Connecticut Light and Power Company

Relocation of Transmission Structure #1966

Staff Report

October 16, 2008

On September 9, 2008, Northeast Utilities Service Company (NU), as an agent for The Connecticut Light and Power Company (CL&P), submitted a petition to the Connecticut Siting Council (Council) for a determination that no Certificate of Environmental Compatibility and Public Need would be required for the relocation of transmission structure #1966 in the town of Woodbury.  On October 7, 2008, Council member Edward Wilensky and Robert Mercier of Council staff met with CL&P representatives Susan Provost, and Thomas Moen and the Town of Woodbury Public Works Director, David Monckton, at the site to review the proposed project.

The project site is located east of Nonnewaug Road and south of Falls Road in Woodbury.  Transmission line #1238 traverses the area in an east-west direction, passing over the Nonnewaug River.  Transmission structure #1966 sits directly in the riverbed due to movement of the river eastward over the years.  The structure, a 95-foot monopole, has become unstable due to river scouring.  Guy wires have been installed to provide temporary support to the monopole.

CL&P proposes to relocate the monopole 110 feet west of its current location using a stationary crane.  The monopole would be direct buried at the edge of a cultivated field to the west of the original location.  The work would require a line shutdown of approximately one week which is anticipated to occur either the first or second week of November.  A power redistribution plan would be in effect.

The relocated structure would be placed in an upland area at the edge of a cornfield.  Disturbance to the stream would be limited to the crane being placed adjacent to the stream bank as well as riverbed disturbance due the pole being removed.  Hay bales would be placed in the river on the downstream side of the pole prior to removal to control sediment.  Once removed, the resulting hole in the riverbed would be left to fill in naturally.  Construction mats would be used as appropriate to control erosion and minimize soil disturbance.