Petition No. 895

Connecticut Light & Power

New Fairfield, Connecticut

Staff Report

April 28, 2009

On April 13, 2009, Northeast Utilities Service Company, acting as agent for Connecticut Light and Power Company (CL&P), filed a petition for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need is required for proposed modifications to an existing SBA monopole wireless communications tower at the Girl Scout Camp on Bogus Hill Road in New Fairfield, Connecticut. Council member Ed Wilensky and Council staff member David Martin conducted a field review of this project on April 27, 2009.  Helen Taylor, Brian Rockwood, Steve Florio, and John D’Ambra represented CL&P at the field review.

CL&P seeks to add three antennas to the existing tower. The antennas would include two whip antennas that would be installed at 93 feet above ground level and one dipole antenna that would be installed at 92 feet above ground level. CL&P would keep its ground equipment inside a 10-foot by 12-foot shelter that would also house a 17 kW propane-fueled generator. The equipment shelter and propane tank would be located in the southeast corner of the existing compound. The generator has been sized to accommodate a request from the Town of New Fairfield to use its power for antennas the town is planning to add to the tower.

CL&P’s antennas would fill an existing coverage gap in its low band voice communications system that provides communications between utility field crews and local dispatch operators. This system is used for daily operations and during storm events.

Currently, the SBA tower has T-Mobile antennas at 150 feet, Cingular antennas at 140 feet, and Verizon antennas at 120 feet. An engineering analysis concluded that the tower has the structural capacity to accommodate CL&P’s proposed antennas.

With the addition of CL&P’s antennas, the power density levels of all the antennas on the tower would equal approximately 28% of the maximum permissible emissions.