Petition No. 901

CMEEC

37 Camp Moween Road, Lebanon

Staff Report

June 4, 2009

On May 7, 2009, the Connecticut Siting Council (Council) received a petition (Petition) from the Connecticut Municipal Electric Energy Cooperative (CMEEC) for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need is required for the proposed installation of two 2.5 MW fuel oil-fired generating units off of Camp Moween Road in Lebanon.  Specifically, CMEEC would install each generator on its own 56-foot by 14-foot concrete pad approximately 66 feet north of Camp Moween Road on the property of the Southeastern Council on Alcoholism and Drug Dependence (SCADD).

The generators would be located inside an approximately 92-foot by 80-foot fenced compound.  Each generator would have a 4,000-gallon double-walled fuel tank with automatic leak detection.  A 3,050-gallon urea tank would be located on a concrete pad in between the two generators and would be used as part of the selective catalytic reduction (SCR) system.  The SCR would reduce nitrogen oxide emissions by 90 percent.  CMEEC has applied for a New Source Review Permit from the Department of Environmental Protection which would permit the plant to provide peaking power in the range of 500 to 1,200 hours per year.

Utilities would run underground to reach a riser location on an existing pole on Camp Moween Road.  The access is already cleared due to existing underground water utilities.

Some limited tree clearing in the vicinity of the proposed compound would be necessary including the removal of two maple trees, 14-inches diameter and 16-inches diameter respectively.  The wood would be harvested and consumed in wood stoves that heat the SCADD building.  Approximately 30 evergreens would be planted along the south / southwest sides of the compound to screen the view of the project from Camp Moween Road.

The nearest residence is on the opposite side of Camp Moween Road and is a least 300 to 400 feet away from the proposed project.  The applicant has provided notice to abutting property owners and no replies were received.

Noise levels of approximately 72 dBA or less at 5 to 21 feet from the units area expected.  However, these levels would drop to less than the noise standard of 51 dBA at the nearest receptor.

The project was field reviewed by Council member Brian Golembiewski and Mike Perrone of the Council staff on May 18, 2009.  Glen Wilson, representing CMEEC, and Jack Malone, Executive Director of SCADD, also attended the field review.

By letter dated May 19, 2009, the Town of Lebanon submitted a letter with conditions that CMEEC agreed to at the May 18, 2009 Planning and Zoning meeting.  These conditions include no signage outside of the project’s fence, no light sources visible outside of the property, additional trees for screening, and the submittal of a Spill Prevention Control Countermeasure Plan (to protect the Yantic River) and fuel tank plans for review by the Lebanon Fire Marshall.