Petition No. 947A

Iroquois Gas Transmission System L.P.

Milford, Connecticut

Staff Report

April 28, 2011

On April 6, 2011, the Connecticut Siting Council (Council) received a petition from Iroquois Gas Transmission System, L.P. (Iroquois) to modify the existing odorant system on the Iroquois pipeline located at 840 Oronoque Road, Milford, Connecticut.  The project is under the exclusive jurisdiction of the Federal Energy Regulatory Commission (FERC).  Iroquois filed the petition to the Council in accordance with a FERC policy requiring applicants to cooperate with state and local agencies in siting pipeline facilities.

The existing Iroquois Compressor Station was reviewed by the Council in Petition 815 and recommendations were sent to FERC on November 30, 2007.

The proposed odorant system is defined by FERC as an “auxiliary installation” and would require no additional approvals from FERC.

Iroquois proposes to modify the existing odorant system by:

- Replacing the existing five gallon odorant tank with a 500-gallon above ground tank enclosed within an aluminum structure with 110 percent spill containment.  The aluminum structure would be 11 feet long by 5 feet wide by 6 feet high.

- Installing an approximately 12-foot by 14-foot concrete vault around the mainline to contain odorant injection piping and a meter transducer to measure gas flow.

- Upgrading a pump cabinet located within the existing utility shed, which will allow the system to be automated and reduce frequency of filling the odorant tank.

The proposed odorant system would be installed on a 4.8-acre property at 840 Oronoque Road in Milford, which is the site of existing Iroquois Compressor and Metering Stations.  The proposed equipment would be installed in the southeastern portion of the property near the existing odorant enclosure.

The property is located in an industrial zone.  Surrounding land uses include a railroad and landfill to the east, O&G Industries Milford Asphalt Plant No. 13 to the south and Oronoque Road and the Connecticut Resource Recovery Authority to the west and north.

Iroquois has received zoning permit and has applied for a building permit from the City of Milford.