NOTICE TO CONTRACTOR – RECENT REVISIONS

The Contractor is hereby notified that the following Traffic Engineering Special Provisions have been revised:

Section 1.07 – Legal Relations and Responsibilities

- Updated service entrance inspection requirements.

Section 10.00 – General Clauses for Highway Illumination and Traffic Signal Projects

- Added email information for digital PDF files

- Updated as-built plan requirements

- Added testing for video detection

1015034A – Grounding and Bonding

- Added new Special Provision for grounding and bonding procedure.

1105xxxA – X_Way_X_Section Traffic Signal:

- Painting requirements for housing, brackets, and hardware have been moved to Form 818.

- Changed LED lens to 15 years warranty type.

- Backplates:

- changed to louvered

- changed retroreflective strip sheeting type

- changed aluminum alloy to 5052-H32

- provided range for acceptable thickness

- U-turn indications have been included.

1105xxxA – LED Traffic Signal Lamp Unit:

- Changed LED lens to 15 years warranty type.

- Items for U-turn indications have been added.

1106xxxA – X_Way_Pedestrian Signal:

- Painting requirements for housing, brackets, and hardware have been moved to Form 818.

1107011A – Accessible Pedestrian Signal and Detector (Type A)

- Painting requirements for housing, brackets, and hardware have been moved to Form 818.

- Changed the sign size to 9” x 15”

- Changed to include confirmation light

1108115A – Full Actuated Controller 8 Phase

- This item has been replaced with Item 1108117A – Full Actuated Controller W/Actuated Pedestrian Phase (16 phase)

1108163A – Modify Existing Controller

- Added email information for digital PDF files

- Added duplex receptacles for detection equipment

1112285A – Thermal Video Detector Assembly

- Clarified the site surveys are to be conducted in the field.

1112286A – 360 Degree Camera Assembly

- Added installation best practices guide

- Clarified the site surveys are to be conducted in the field.

1118012A – Removal and/or Relocation of Traffic Signal Equipment

- Added line indicating salvage of State-owned traffic signal equipment shall be coordinated with District Electrical Maintenance.

The Contractor is hereby notified that the following Traffic Engineering Special Provisions have been newly added:

1108110A – Traffic Signal Controller

1111471A – GPS Coordination Unit

1105XXA – X Way, X Section Traffic Signal Polycarbonate

The Contractor is hereby notified that the following Traffic Engineering guide sheets are included:

GS_Light Standard and Foundation

- Added J-Hook Mounting Detail.

- Added Aluminum Light Standard Base showing Grounding Lug Detail.

- Added Portland Cement concrete number.

GS_Traffic Control Foundations

- Added Portland Cement concrete number.

GS_Concrete Handhole

- Added Portland Cement concrete number.

The Contractor is hereby notified that the following Traffic Engineering Special Provision is no longer required. All pertinent information is included in the Form 818:

1001001A – Trenching and Backfilling