# STATE OF CONNECTICUT

# DEPARTMENT OF ENERGY & ENVIRONMENTAL PROTECTION

# OFFICE OF ENVIRONMENTAL REVIEW

# 79 ELM STREET, HARTFORD, CT 06106-5127

To:	Eric McPhee - Supervising Sanitary Engineer

DPH - Drinking Water Section, 450 Capitol Avenue, MS#51WAT, Hartford

From:	David J. Fox - Senior Environmental Analyst	Telephone:   860-424-4111

Date:	March 7, 2013	E-Mail:  david.fox@ct.gov

Subject:	Deep River Pumps & Tanks, Lebanon

The Department of Energy & Environmental Protection (DEEP) has received the Notice of Scoping for the proposed construction of two water storage tanks off Lynch Road in Lebanon and upgrades to the pumps at the Deep River water treatment plant.  The following comments are submitted for your consideration.

The Deep River water treatment plant has a registered diversion pursuant to section 22a-368 of the Connecticut General Statutes (CGS).  If the proposed upgrades to the pumps will result in an increase in their pumping capacity, the Inland Water Resource Division should be contacted to determine whether a diversion permit would be required.  For further information, contact Doug Hoskins at douglas.hoskins@ct.gov or at 860-424-4192.

As shown on the aerial photo provided, the proposed tanks are immediately north of Lynch Road.  Land immediately to the south of Lynch Road is DEEP property, Mooween State Park.  Any work proposed south of the road, may require property rights from DEEP.  If so, an application must be completed and submitted to DEEP Land Acquisition and Management.  The application can be obtained by contacting DEEP Land Acquisition and Management at 860-424-3016.  Submitted applications are reviewed by a multi-disciplined committee that will make its recommendations regarding the application to the Commissioner of DEEP.  If approved by the Commissioner, the applicant will then have to negotiate the terms and necessary legal document(s) with DEEP.

If the tanks are to be tested and disinfected, the discharge would be covered by the General Permit for the Discharge of Hydrostatic Pressure Testing Wastewater (DEP-PERD-GP-011).  This general permit applies to all discharges of waters used to test the structural integrity of new or used tanks and pipelines that hold or transfer drinking water, sewage, or natural gas.  The general permit contains pH, chlorine, oil and grease, and suspended solids limits which will need to be complied with during the testing and verified through monitoring.  Registration is required to be submitted to the Department in order for the discharges to be authorized by this general permit.  A fact sheet, the general permit which includes the registration form, titled Notice of Coverage, and the Application Transmittal form may be downloaded at: Hydrostatic GP

The Natural Diversity Data Base, maintained by DEEP, contains no records of extant populations of Federally listed endangered or threatened species or species listed by the State, pursuant to section 26-306 of the CGS, as endangered, threatened or special concern at the project area.  This information is not the result of comprehensive or site-specific field investigations.  Also, be advised that this is a preliminary review.  A more detailed review may be conducted as part of any subsequent environmental permit applications submitted to DEEP for the proposed site.  Consultation with the Natural Diversity Data Base should not be substituted for on-site surveys required for environmental assessments.  The extent of investigation by competent biologist(s) of the flora and fauna found at the site would depend on the nature of the existing habitat(s).  If field investigations reveal any Federal or State listed species, please contact the DEEP Geologic & Natural History Survey at 860-424-3540.

Thank you for the opportunity to review this project.  If there are any questions concerning these comments, please contact me.

cc:	Robert Hannon, DEEP/OPPD

Doug Hoskins, DEEP/IWRD

Al Schwentke, DEEP/LAM