# STATE OF CONNECTICUT

# DEPARTMENT OF ENERGY & ENVIRONMENTAL PROTECTION

# OFFICE OF ENVIRONMENTAL REVIEW

# 79 ELM STREET, HARTFORD, CT 06106-5127

To:	Eric McPhee - Supervising Environmental Analyst

DPH - Drinking Water Section, 450 Capitol Avenue, MS#51WAT, Hartford

From:	David J. Fox - Senior Environmental Analyst	Telephone:   860-424-4111

Date:	February 7, 2013	E-Mail:  david.fox@ct.gov

Subject:	Spring Hill Reliability Project, Norwalk & New Canaan

The Department of Energy & Environmental Protection has received the Notice of Scoping for the project proposed by the Norwalk First Taxing District to construct a storage tank, booster pump station and piping improvements in the Spring Hill section of Norwalk and install a water main at Mill Road in New Canaan.  The following comments are submitted for your consideration.

The water main along Mill Road in New Canaan is within the 100-year flood zone on the community's Flood Insurance Rate Map.  Because it is a State action, the project must be certified by DPH as being in compliance with flood and stormwater management standards specified in section 25-68d of the Connecticut General Statutes (CGS) and section 25-68h-1 through 25-68h-3 of the Regulations of Connecticut State Agencies (RCSA) and receive approval from the Department.  For further information, contact the Inland Water Resources Division at 860-424-3706.  A fact sheet regarding floodplain management and the certification form can be downloaded at: Flood Management.

Any inland wetlands or watercourses at the site are regulated by the local inland wetlands agency, pursuant to section 22a-42 of the CGS.  Many local agencies have established setback or buffer areas and require review and approval of activities within these upland areas adjacent to wetlands or watercourses.  The local agency should be contacted regarding permit requirements.

In order to protect wetlands and watercourses on and adjacent to the site, strict erosion and sediment controls should be employed during construction.  The Connecticut Guidelines for Soil Erosion and Sediment Control prepared by the Connecticut Council on Soil and Water Conservation in cooperation with DEEP is a recommended source of technical assistance in the selection and design of appropriate control measures.  The 2002 revised edition of the Guidelines is available online at:  Erosion Control Guidelines.

If the water mains are to be tested and disinfected, the discharge would be covered by the General Permit for the Discharge of Hydrostatic Pressure Testing Wastewater (DEP-PERD-GP-011).  This general permit applies to all discharges of waters used to test the structural integrity of new or used tanks and pipelines that hold or transfer drinking water, sewage, or natural gas.  The general permit contains pH, chlorine, oil and grease, and suspended solids limits which will need to be complied with during the testing and verified through monitoring.  Registration is required to be submitted to the Department in order for the discharges to be authorized by this general permit.  A fact sheet, the general permit which includes the registration form, titled Notice of Coverage, and the Application Transmittal form may be downloaded at: Hydrostatic GP

Stormwater discharges from construction sites where one or more acres are to be disturbed require a permit pursuant to 40 CFR 122.26.  The Permitting & Enforcement Division has issued a General Permit for the Discharge of Stormwater and Dewatering Wastewaters Associated with Construction Activities (DEP-PERD-GP-015) that will cover these discharges.  For projects disturbing five or more acres, registration describing the site and the construction activity must be submitted to the Department prior to the initiation of construction.  A stormwater pollution control plan, including measures such as erosion and sediment controls and post construction stormwater management, must be prepared.  For sites where more than 10 acres will be disturbed, the plan must be submitted to the Department.  A goal of 80 percent removal of total suspended solids from the stormwater discharge shall be used in designing and installing post-construction stormwater management measures.  For construction projects with a total disturbed area between one and five acres, no registration is required as long as the project is reviewed by the town and receives written approval of its erosion and sediment control measures and it adheres to the Connecticut Guidelines for Soil Erosion and Sediment Control.  If no review is conducted by the town or written approval is not provided, the permittee must register with the Department.  For further information, contact the division at 860-424-3018.  A copy of the general permit as well as registration forms may be downloaded at: Construction Stormwater GP.

Development plans for utilities in urban areas that entail soil excavation should include a protocol for sampling and analysis of potentially contaminated soil.  A soil management plan should be developed for the project to deal with soils during construction.  The Department’s Guidance for Utility Company Excavation should be used a guide in developing the plan.  The guidance is available on-line at: Utility Guidance .

The Natural Diversity Data Base, maintained by DEEP, contains no records of extant populations of Federally listed endangered or threatened species or species listed by the State, pursuant to section 26-306 of the CGS, as endangered, threatened or special concern at either project area.  This information is not the result of comprehensive or site-specific field investigations.  Also, be advised that this is a preliminary review.  A more detailed review may be conducted as part of any subsequent environmental permit applications submitted to DEEP for the proposed site.  Consultation with the Natural Diversity Data Base should not be substituted for on-site surveys required for environmental assessments.  The extent of investigation by competent biologist(s) of the flora and fauna found at the site would depend on the nature of the existing habitat(s).  If field investigations reveal any Federal or State listed species, please contact the DEEP Geologic & Natural History Survey at 860-424-3540.

Thank you for the opportunity to review this project.  If there are any questions concerning these comments, please contact me.

cc:	Jeff Caiola, DEEP/IWRD

Robert Hannon, DEEP/OPPD