| Skill No. | 5.3.10D | Primary Task: | Charged Hoseline Operation from Ground Ladder |
| --- | --- | --- | --- |
| Objective(s) : | 5.3.10, 5.3.10(B) | NFPA Standard: | 1001 Candidate # |  |
| Performance Evaluation Sheet |
| Task |
|  | 1st | 2nd |
| 1 | * Wears full protective equipment properly |  |  |
| 2 | Ascends ladder safely with charged hose line |  |  |
| 3 | * Maintains communication |  |  |
| 4 | Assures proper position on ladder for best penetration |  |  |
| 5 | * Uses leg lock |  |  |
| 6 | Projects nozzle between rungs for best results |  |  |
| 7 | Uses hose strap to secure hose to ladder |  |  |
| 8 | * Slowly opens nozzle and flows water safely |  |  |
| * Critical Task | Failure of this task mandates failure on the entire objective | Safety is PARAMOUNT | Total number tasks candidate must complete to pass | 6 |