| Skill No. | 5.3.1E | Primary Task: | SCBA – Ready for Immediate Use |
| --- | --- | --- | --- |
| Objective(s) : | 5.3.1, 5.3.1(B) | NFPA Standard: | 1001 | Candidate # |  |
| Performance Evaluation Sheet |
| Task |
|  | 1st | 2nd |
| 1. | * Checks that cylinder is full (or at least 90%) |  |  |
| 2. | Checks operation of all gauges. Verifies that difference between cylinder and regulator gauge does not exceed 100 psi. |  |  |
| 3. | Tests operation of low pressure alarm |  |  |
| 4. | Checks all hose connections |  |  |
| 5. | Checks condition of facepiece |  |  |
| 6. | Checks condition of harness and straps |  |  |
| 7. | Checks operation of mainline and bypass valves ( if applicable ) |  |  |
| 8. | Checks that unit is clean and sanitized |  |  |
| 9. | * Tests PASS device ( if applicable ) |  |  |
| * Critical Task | Failure of this task mandates failure on the entire objective | Safety is PARAMOUNT | Total number tasks candidate must complete to pass | 7 |