Petition No. 1025

The Connecticut Light and Power Company

Staff Report

March 29, 2012

On February 22, 2012, the Connecticut Siting Council (Council) received a petition (Petition) from The Connecticut Light and Power Company (CL&P) for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need is required to modify an existing substation at 2225 River Road, Southbury.  This Petition was field reviewed by Council member Larry Levesque and Michael Perrone of the Council staff on March 2, 2012.  Rina Landry, Helen Taylor, and Kenneth Case from CL&P also attended the field review.

Specifically, CL&P seeks to replace and re-locate an existing 67 MVA autotransformer at the Shepaug Substation.  (See picture below.)  The existing autotransformer is over 60 years old and in need of replacement.  Furthermore, it is located too close to the control house to meet current code requirements.  As such, the old autotransformer would be removed, and the new one would be installed approximately 131 feet to the west of the existing transformer location.  A new concrete foundation pad, oil containment system, and auxiliary power facilities for the new autotransformer would also be installed.  A new bus configuration would be installed to accommodate the new autotransformer.

All work would remain within the existing fenced substation.  No wetlands are located at the project site.  The new equipment would be similar in appearance to that of the existing equipment.  The site is fairly remote so the visual impact is expected to be minimal.  No material change in sound levels is expected.  The proposed project is not located within a 100-year or 500-year flood plain.

If approved, construction would begin during spring 2012 and would be completed by October 2012.