Petition No. 1032

The Connecticut Light and Power Company

Norwalk Substation

Staff Report

August 9, 2012

On July 3, 2012, the Connecticut Siting Council (Council) received a petition (Petition) from The Connecticut Light and Power Company (CL&P) for a declaratory ruling that no Certificate of Environmental Compatibility and Public Need is required to modify an existing substation located at 50 New Canaan Avenue in Norwalk.  The modifications are necessary to meet future capacity needs in the Norwalk area.  A field review of the petition was conducted on August 3, 2012 by Council member Dr. Barbara Bell, Council staff member Robert Mercier, and CL&P representatives Helen Taylor, Kris Aberg, and Amanda Mayhew.

CL&P seeks to install the following:

  - one 115-kV bus circuit breaker and associated disconnect switch;

  - two termination structures and associated lighting arresters, duct-banks, cabling, and protection and control equipment;

  - one 115- to 13.8-kV, 60 MVA distribution transformer;

  - one 13.8-V switchgear with one transformer position; and

  - one monopole terminal structure in place of two A-frame terminal structures.

All work would occur in the southwest corner of the existing, fenced substation.    The project would require a Department of Energy and Environmental Protection General Permit notification as the work area is within the Norwalk River stream encroachment boundary.  Environmental controls during the project would include erosion and sediment controls, appropriate dewatering procedures, and soil characterization.  No visual impact would occur as the site is isolated from surrounding properties by roads and the Norwalk River corridor.  Additionally, the proposed equipment would be similar in appearance and height to that of existing substation equipment.