Petition No. 310HW

Safety-Kleen Corp.

Staff Report

April 2, 1997

On  March 25, 1997, Connecticut Siting Council (Council) members Dr. William Smith and Edward Wilensky, and Council Staff Joel Rinebold, Fred Cunliffe, and Paul Aresta met Safety-Kleen Corp. representatives Thomas Heaton and Donald Zielinski for a site inspection of  Safety-Kleen’s service center located at 24 Brixton Street, West Hartford. Safety-Kleen is amending their petition for a declaratory ruling that no Certificate of Public Safety and Necessity (Certificate) is required for proposed changes to their existing facility. Safety-Kleen operates an interim status facility for the temporary storage of hazardous waste. Safety-Kleen proposes to install a 12,000 gallon, aboveground tank for the temporary storage of parts washer solvent waste. This new tank is proposed to replace one of the two existing 12,000 gallon, underground tanks which was taken out of service on February 12, 1997, due to the discovery of holes in the primary containment.

On July 14, 1993, the Council determined that certain changes to Safety-Kleen’s service center located at 24 Brixton Street did not require a Certificate.  On May 10, 1995, the Council rendered a concurring determination that operations on a contiguous parcel of land would not require a Certificate. On May 21, 1996, the Council considered changes to the original proposal of July 14, 1993, and determined that a Certificate was not required. Safety-Kleen is continuing to work with the Department of Environmental Protection to finalize the 10-day transfer facility permit.

The proposed 12,000 gallon, aboveground tank will be placed adjacent to the existing 3-bay return/fill station.  The proposed tank will be double-walled, and will have a high-level alarm and mechanical float shut-off valve to prohibit accidental spillage. There will be no increase in hazardous waste storage capacity as the proposed tank will be removed from service upon the commencement of operation of the 10-day transfer facility.

Actions which may not require a Certificate from the Council include changes or alterations of a facility which do not constitute a “modification. The “routine maintenance, repair, or replacement of the individual components at a hazardous waste facility that is necessary for normal operation or a change or alteration at a hazardous waste facility ordered by a state official in the exercise of his statutory authority shall not be deemed to be a modification” (General Statutes ( 22a-115 (9)). Safety-Kleen contends that the proposed change will not increase the volume or change the composition of hazardous waste at the existing facility, and is a replacement of an individual component.