Petition No. 364

Connecticut Light & Power Company

Staff Report

November 21, 1996

On November 4, 1996, the Connecticut Light and Power Company (CL&P), petitioned the Connecticut Siting Council (Council) for proposed modifications within the existing Montville Substation located off Powerhouse Road in Montville, Connecticut.  CL&P proposes to install a 115-kV, a 100 MVAR capacitor bank, a circuit breaker, three current-limiting reactors, two circuit switchers, a disconnect switch, and associated protective relay and control equipment.  All proposed additions would be lower in height than existing substation structures; would visually blend into the background of station structures; would not increase sound levels; would not be located in a 100-year flood zone, stream encroachment line, wetland, or waterway; would not contain PCB’s; and would not create radio or TV interference.

The proposed project and other related projects would allow CL&P to support voltage and increase the import of approximately 150 to 300 MW of electricity into Connecticut from generation sources outside the State.  The project is part of CL&P’s plans to reinforce the transmission system in preparation for alleviating Connecticut generation shortages during peak periods.

Construction would commence during November 1996, and be completed by the end of May 1997.

JMR:TEF:mmb