Petition No. 368

Connecticut Light & Power Company

Frost Bridge Substation

Staff Report

February 5, 1997

On January 24, 1997, the Connecticut Light and Power Company (CL&P) petitioned the Connecticut Siting Council for proposed modifications within the existing Frost Bridge Substation, located off Frost Bridge Road in Watertown, Connecticut.  CL&P proposes to install a 115-kV, 50 MVAR capacitor bank, one circuit switcher, and associated protective relay and control equipment on the west side of the substation.  All proposed additions would be lower in height than existing substation structures; would visually blend into the background of station structures; would not increase sound levels; would not be located in a 100-year flood zone, stream encroachment line, wetland, or waterway; would not contain PCB’s; and would not create radio or TV interference.

The proposed project and other related projects would allow CL&P to support voltage along existing transmission lines from importation of electricity into Connecticut during the time the Long Island Sound 138-kV submarine transmission line is out of service.

Construction is expected to commence in February 1997, and to be completed by the end of June 1997.

Thomas E. Fanning, Jr.

Siting Analyst

TEF:mmb