Petition No. 369

Connecticut Light & Power Company

Waterside Substation

Staff Report

February 5, 1997

On January 24, 1997, the Connecticut Light and Power Company (CL&P) petitioned the Connecticut Siting Council for proposed modifications within the existing Waterside Substation, located off Bonner Street in Stamford, Connecticut.  CL&P proposes to install a 115-kV, 40 MVAR capacitor bank, one circuit breaker, three current-limiting reactors, two disconnect switches, associated protective relay and control equipment, and would extend the 115-kV bus on the east side of the substation.  All proposed additions would be lower in height than existing substation structures, would visually blend into the background of station structures, would not increase sound levels, and would not be located in a 100-year flood zone or stream encroachment line.  No wetland or waterway would be negatively affected.  The proposed equipment would not contain PCB’s and would not create radio or TV interference.

The proposed project and other related projects would allow CL&P to support voltage along existing transmission lines from importation of electricity into Connecticut during the time the Long Island Sound 138-kV submarine transmission line is out of service.

Construction is expected to commence in February 1997, and to be completed by the end of June 1997.

Thomas E. Fanning, Jr.

Siting Analyst

TEF:mmb