Petition No. 372HW

Uniroyal Chemical Company, Inc.

Staff Report

June 3, 1997

On May 30, 1997, Connecticut Siting Council (Council) members Gloria Dibble Pond and Edward Wilensky, and Council Staff Joel Rinebold, Robert Erling, and Paul Aresta met Uniroyal Chemical Company, Inc., (UCC) representatives Jim Heidenriech and George Kochera for a site inspection of a portion of UCC’s facility located at 280 Elm Street, Naugatuck. The UCC facility is comprised of approximately 90 buildings and manufactures over one hundred different chemical products. UCC is petitioning for a declaratory ruling that no Certificate of Public Safety and Necessity (Certificate) is required for changes to their existing facility.

UCC has replaced an existing 10 ft x  32 ft temporary drum storage area with two new containment structures: one 20 ft x 10 ft  for the temporary storage of (32) thirty-two 55 gallon drums, and another 50 ft x 14 ft for the loading of a tank truck with hazardous waste nonene liquids or cyclohexene. UCC removed the 10 ft by 32 ft asphalt pad used for temporary drum storage in January of 1997,  which had the capacity for (64) sixty-four 55 gallon drums, to construct the two new containment structures. Both containment structures are constructed of concrete, 6-8 inches thick, and all expansion joints are sealed with a chemical resistant sealer (SIKAFLEX-10). The containment structures are three sided and slope away from the opening towards a sump at the opposite end. The sumps are connected to the facility’s pre-treatment system prior to being treated at the Naugatuck treatment works. Two stainless steel pipes (1 1/2” and 2”) will be used for the transfer of cyclohexene. These pipes run overhead, from the cyclohexene storage tank, along the rear or west side of the new structures. The pipe used for the transfer of the hazardous waste nonene liquids will be a 4” flex-hose, which will run along the ground against the outside of the south wall. The former temporary drum storage area and contaminated underlying soils were removed; however, formal closure of this area has not been concluded. The Connecticut Department of Environmental Protection is aware of the new construction and has jurisdiction under the Resources Conservation and Recovery Act to regulate the operations at this facility.

UCC contends that the improvements to their facility encompass the repair and replacement of individual components of a hazardous waste facility necessary for normal operation, and do not constitute a “modification” as defined in Section 22a-115(9).  UCC further contends that the improvements are related to short-term storage and do not constitute disposal of a hazardous waste, there will be no increase in the volume of waste, and the improvements do not encompass the storage of new waste streams.