Petition No. 376

Hamilton Standard

Division of United Technologies Corporation

Staff Report

June 30, 1997

On June 30, 1997, Connecticut Siting Council (Council) member Colin C. Tait and Council staff Joel M. Rinebold and Paul Aresta met Hamilton Standard representative Jonathan Katz and ONSI Corporation representative Leon Botterman for a site inspection of the proposed 200 kW fuel cell in Windsor Locks.  Hamilton Standard is petitioning for a declaratory ruling that no Certificate of Public Safety and Necessity (Certificate) is required for changes to their emergency generating system at Hamilton Standard’s Data Center in Windsor Locks. The proposed fuel cell was placed on a concrete base at the Hamilton Standard facility, however, final service connections are absent.

Hamilton Standard proposes to add a 200 kW fuel cell as the primary source of electricity to the data center and a new 500 kW Cummins diesel generator for back up. The proposed fuel cell is planned to augment an emergency generating facility by furnishing electricity in such a manner as to enhance the reliability of the electrical supply.

The proposed fuel cell, Model PC25tm C, is fueled by natural gas and generates electricity, heat, and water.

The proposed fuel cell is 10 feet x 18 feet and is 10 feet tall.

The proposed fuel cell has a noise signature which is comparable to a window air conditioner ( 60 dB at 30 feet).

The proposed fuel cell will not require a new source review permit from the Department of Environmental Protection.

The proposed fuel cell site is in a commercial area.

Hamilton Standard contends that the proposed changes to the emergency generating system will not result in a substantial adverse effect on the environment. Hamilton Standard contends that the fuel cell power plant is inherently clean, quiet, and highly efficient. Hamilton Standard also contends that aesthetically, the proposed fuel cell will be an insignificant addition to their facility.