Petition No. 396

East Lyme, Connecticut

Omnipoint Communications Inc.

Staff Report

July 9, 1998

On June 22, 1998, the Connecticut Siting Council (Council) Executive Director, Joel M. Rinebold, Council members Brian Emerick and Ed Wilensky, and Paul Aresta and Robert Erling of the Council Staff met with Sharon Burrows, Kenneth Jenkins, Michael Lund, Steven Lingard and Brian Weinstein of Omnipoint Communications, Inc. (Omnipoint) for a field review on a petition in the Town of East Lyme, Connecticut.  Omnipoint is petitioning the Council for a determination that no Certificate of Environmental Compatibility and Public Need (Certificate) would be required for modifications to an existing Connecticut Light and Power (CL&P) electric transmission line facility in East Lyme.  Omnipoint submits no Certificate would be required because the addition of the antenna and associated equipment would not have a substantial adverse environmental effect.

Omnipoint proposes to attach one antenna to existing 90-foot CL&P monopole structure number 6076 located off of King Arthur Drive in East Lyme.  Access to the site would be through the parking lot of Motel 6, which stands approximately 120 feet to the west.  A temporary 15-foot by 20-foot staging area would be placed immediately south of the base of the tower.  The PCS antenna would be placed at the top of the tower with the top of the antenna being 100 feet above ground level (AGL).  The proposed antenna is 72 inches in height, 16 inches in diameter, and weighs 150 lbs.  To provide utilities, a new pole would be installed outside the motel parking lot, and electric and telephone utilities would be placed underground a distance of approximately 315 feet underground.  The communications equipment would be placed in a cabinet on a 10-foot by 5.5-foot concrete slab near the base of the tower.  Some existing brush would be removed.  The total calculated radio frequency power density at the base of the tower would be 0.0174 mW/cm2, which is 1.74 percent of the maximum permissible exposure for uncontrolled environments based on Federal Communications Commission Bulletin 65, August 1997.