Petition No. 397

Darien, Connecticut

Omnipoint Communications Inc.

Staff Report

July 9, 1998

On June 22, 1998, the Connecticut Siting Council (Council) Executive Director, Joel M. Rinebold, Council members Brian Emerick and Ed Wilensky, and Paul Aresta and Robert Erling of the Council Staff met with Sharon Burrows, Kenneth Jenkins, Michael Lund, Steven Lingard and Brian Weinstein of Omnipoint Communications, Inc. (Omnipoint) for a field review on a petition in the Town of Darien, Connecticut.  Omnipoint is petitioning the Council for a determination that no Certificate of Environmental Compatibility and Public Need (Certificate) would be required for modifications to an existing Connecticut Light and Power (CL&P) electric transmission line facility in Darien.  Omnipoint submits no Certificate would be required because the addition of the antenna and associated equipment would not have a substantial adverse environmental effect.

Omnipoint proposes to attach an antenna to the top of existing 105-foot CL&P transmission line tower structure number 1041 at the Noroton Heights Railroad Station in Darien, Connecticut.  Access would be through the parking lot of the railroad station.  A temporary 15-foot by 20-foot staging area would be used immediately south of the base of the tower.  Construction should last only one day and railroad officials have been notified.  Several existing shrubs would be removed and replaced.  The PCS antenna would be placed at the top of the tower, with the antennas being 113-feet 8 inches above ground level (AGL).  The proposed antenna is 72 inches in height, 16 inches in diameter and weighs 150 lbs.  Communications equipment would be placed on a new 12-foot by 8-foot concrete slab placed east of the base of the tower.  The total calculated radio frequency power density at the base of the tower would be 0.0123 mW/cm2, which is 1.23 percent of the maximum permissible exposure for uncontrolled environments based on Federal Communications Commission  Bulletin 65, August 1997.