Petition No. 398

Wilton, Connecticut

Omnipoint Communications Inc.

Staff Report

July 9, 1998

On June 22, 1998, the Connecticut Siting Council (Council) Executive Director, Joel M. Rinebold, Council members Brian Emerick and Ed Wilensky, and Paul Aresta and Robert Erling of the Council Staff met with Sharon Burrows, Kenneth Jenkins, Michael Lund, Steven Lingard and Brian Weinstein of Omnipoint Communications, Inc. (Omnipoint) for a field review on a petition in the Town of Wilton, Connecticut.  Omnipoint is petitioning the Council for a determination that no Certificate of Environmental Compatibility and Public Need (Certificate) would be required for modifications to an existing Connecticut Light and Power (CL&P) electric transmission line facility in Wilton.  Omnipoint submits no Certificate would be required because the addition of the antenna and associated equipment would not have a substantial adverse environmental effect.

Omnipoint proposes to attach one PCS antenna to the top of existing 105-foot lattice CL&P transmission tower structure number 2983 off of Pimpewaug Road in Wilton.  The top of the antenna would be 115 feet above ground level (AGL).  The proposed antenna is 72 inches in height, 16 inches in diameter and weighs 150 lbs.  Access would be directly off Pimpewaug Road.  A temporary 15-foot by 20-foot staging area would be located west of the existing tower.  A small amount of shrubs and brush would be removed to accommodate the equipment cabinet which would be placed south of the base of the tower on a 10-foot by 5.5-foot concrete slab.  The total radio frequency power density of the base of the tower would be 0.0128 mW/cm2, which is 1.3 percent of the maximum permissible exposure for uncontrolled environments based on Federal Communications Commission  Bulletin 65, August 1997.