Petition No. 400

Omnipoint Communications Inc.

Trumbull, Connecticut

Staff Report

July 23, 1998

On July 13, 1998, Pamela B. Katz and Albert E. Gary of the Connecticut Siting Council (Council) and Fred O. Cunliffe of the Council Staff met with Jay Hogan, Bob Hogan, Kenneth Jenkins, Steven Lingard and Brian Weinstein of Omnipoint Communications, Inc. (Omnipoint) for a field review on a petition in the Town of Trumbull, Connecticut.  Omnipoint is petitioning the Council for a determination that no Certificate of Environmental Compatibility and Public Need (Certificate) would be required for modifications to an existing Connecticut Light and Power (CL&P) electric transmission line support structure in Trumbull.

Omnipoint proposes to attach one PCS antenna to the top of an existing 130-foot steel monopole transmission line support structure (#845) approximately 50 feet east of the Rocky Hill Road cul-de-sac.  The top of the antenna would be about 138 feet eight inches above ground level (AGL).  The proposed antenna is 72 inches in height, 16 inches in diameter and weighs 150 lbs.  A footpath access and underground utilities would be constructed off Rocky Hill Road within the CL&P right-of-way for a distance of about 75 feet. Omnipoint proposes to construct a 10-foot by 5.5-foot concrete slab for an equipment cabinet on the west side of the existing structure.  While Omnipoint proposes to install a 12-foot by 14-foot fence around the equipment cabinet, the footprint for the proposed fence could be reduced or eliminated.  Omnipoint does not require fencing at all of its sites. No wetlands have been identified in the site area.  Erosion and sediment controls would be installed prior to soil disturbance. Other areas disturbed by construction would be raked and seeded.

The propopsed site is in an area zoned residential (A).  Land uses to the north is the Merritt Parkway (Route 15) and the southbound exit to Route 25; east of the site are transmission towers and CL&P right-of-way that cross over Route 25 in an east-west direction; an apartment complex is about 500 feet to the south; and single family residences are to the west with the nearest residence about 200 feet from the proposed site. Some vegetation would need to be cleared to construct the proposed site, but Omnipoint does not propose landscaping because of the heavy vegetation surrounding the proposed site.

The total radio frequency power density of the base of the tower would be 0.0086 mW/cm2, which is 0.86 percent of the maximum permissible exposure for uncontrolled environments based on Federal Communications Commission  Bulletin 65, August 1997.

Omnipoint contends no Certificate would be required because the addition of the antenna and associated equipment would not have a substantial adverse environmental effect.