Docket No. 60A

Transfer of Certificate

and

Petition No. 401

Hartford Steam Company

Hartford Hospital Cogeneration Facility

Hartford, Connecticut

September 24, 1998

Staff Report

On July 17, 1998, Hartford Steam Company (HSC) requested a transfer of their Certificate of Environmental Compatibility and Public Need (Certificate) initially issued to the Flagg Energy Development Corporation in Docket No. 60/60A - construction, maintenance and operation of a cogeneration facility at Hartford Hospital.  HSC acquired this facility on June 26, 1998.  HSC did not contemplate transfer of the original Certificate at or prior to the Certificate being issued to Flagg Energy Development Corporation. HSC currently owns and operates a 4.2 megawatt (MW) gas turbine at the G.Fox building in Hartford (50% partner) and a steam and chilled water facility at 60 Columbus Boulevard, Hartford.  HSC will comply with all applicable terms, limitations, and conditions of the Certificate.

HSC also submitted a petition for a declaratory ruling that no amendment of the Certificate is necessary for the replacement of two gas turbines with one new gas turbine and an auxiliary boiler at the cogeneration facility. The change is being proposed to replace the exisitng equipment which is malfunctioning, and to meet contractual energy obligations to serve Hartford Hospital.  HSC proposes to replace the two existing Allison gas turbines and one duct burner with one Solar Taurus gas turbine and a Clever Brooks auxiliary boiler.  This change in equipment would decrease the electric generating capacity from 16 megawatts (MW) to 7MW.  Further the new equipment would result in an overall decrease in air emissions except for particular matter as shown in Table 1. Air emissions would continue to be discharged through the existing 121-foot stack.  The essential characteristics and footprint of the facility, as approved by the Council in Dockets 60/60A, would remain unchanged.  HSC expects completion of construction in November 1998.

Table 1. Comparison of Maximum Hourly Emissions

| Pollutant | Existing Permit lb/hr | Proposed Permit lb/hr |
| --- | --- | --- |
| PM10 | 6.22 | 7.14* |
| SO2 | 64.5 | 56.03 |
| NOx | 46.38 | 27.39 |
| CO | 396.48 | 52.54 |
| VOC | 93.68 | 10.53 |

* Conservative estimate of the vendor but is expected to be lower.

HSC has submitted an application for air permits to construct and operate a gas turbine with duct burner and auxiliary boiler in April 1998. HSC believes the proposed facility would have less air emissions than the existing facility and the changes would not exceed major source/ major modification thresholds for air emissions. The Department of Environmental Protection has issued a final permit to construct.  Also, HSC is renewing its permits for wastewater, blowdown for heating and cooling, and stormwater.  While the DEP has not finalized its determination on the water discharge permit, HSC does not expect changes to the discharge thresholds.  Water will continued to be supplied by the Metropolitan District Commission.

HSC contends that the routine replacement of individual components does not constitute a modification of a facility or in the alternative, if the Council determines that the proposed replacement of turbines is a modification, such modification would not require a Certificate because it would not cause a substantial environmental effect.