Petition No. 403

Sprint Spectrum, L.P.

Beacon Falls, Connecticut

Staff Report

November 5, 1998

On Tuesday, November 3, 1998, Connecticut Siting Council (Council) members Edward S. Wilensky and Gerald Heffernan, and Council staff Fred O. Cunliffe and Joel M. Rinebold met Sprint Spectrum L. P.’s (Sprint) representatives Karen Johnson, John Tierney, and Julie Cashin, for a site inspection of the proposed modification to an existing Connecticut Light and Power Company’s (CL&P) electric transmission line support structure (#326) located at 242 Pent Road, Beacon Falls, Connecticut.  Sprint is petitioning the Council for a declaratory ruling that modifications to this existing transmission line support structure and placement of equipment at the base of the structure would not have a substantial adverse environmental effect. Sprint currently provides coverage to the north along Route 8 from a monopole tower located in Naugatuck, and to the south along Route 8 from a monopole tower located in Seymour.

Sprint proposes to construct a Fort Worth Tower PowerMount( (Power Mount), with a triangular platform supporting antennas measuring 60 inches by 6.1 inches by 2.8 inches at a centerline height of 97.5 feet above ground level (AGL), within the existing CL&P transmission line structure (#326).  Sprint would also install three equipment cabinets measuring approximately 31 inches by 30 inches by 66 inches in height, on an 8-foot by 11-foot concrete pad north of the existing structure’s foundation footprint, and construct a six-foot fence topped with three strands of barbed wire around the equipment and Power Mount. A GPS antenna would be installed on a pole within the compound.  The proposed Power Mount with antennas would extend approximately 18 feet above the top of the 82-foot high transmission line support structure for a total height of approximately 100 feet AGL.

Since CL&P transmission line easement is limited to an aerial right-of-way, Sprint will enter into a ground lease agreement with the Darlene and Carol Griska for use of the property.  Access to the CL&P structure would be 260 feet from Pent Road over the Griska’s driveway.  Utilities would be placed underground from an existing distribution pole approximately 750 feet to a new transformer to be located at the Griska’s driveway entrance and continue underground within the Griska’s driveway. Sprint would construct a new 50-foot gravel-covered access drive to the structure. Sprint would restore the Griska’s driveway to its original condition after construction.

Wetlands have been identified parallel to Pent Road and on either side of the Griska driveway.  An existing 30-inch reinforced concrete pipe and associated fill embankments allow for an intermittent watercourse to flow under the driveway.  Erosion and sediment controls would be placed on the west side of the driveway and along the south and west perimeters of the site prior to construction.

Surrounding land uses include a CL&P substation 2,000 feet east of ther proposed site and transmission lines, a Town-owned recreation facility across Pent Road, and two single-family residential structures Griska’s property.  The zoning of this area is residential.  The existing transmission line structure to the east would not provide adequate coverage, and the transmission structure to the west would be difficult to access because of steep slopes.

The proposed construction of a Power Mount and associated antennas and equipment within CL&P’s existing transmission line structure would not exceed the maximum permissible exposure limit for the worst case radio frequency power density at the base of the structure (5.24% of the standard).  Sprint contends that the proposed modifications to CL&P’s existing facility or placement of equipment on Griska’s property will not cause a substantial adverse environmental effect and does not require a Certificate from the Council.  Furthermore, Sprint will not have a need to construct a new tower in the project area if the Council determines that no Certificate is required.