Petition No. 404

Omnipoint Communications, Inc.

Woodbridge, Connecticut

Staff Report

December 17, 1998

On December 15, 1998, Connecticut Siting Council (Council) Executive Director, Joel M. Rinebold, Council member Brian Emerick and Robert Erling of the Council staff met J. Brendon Sharkey, Haider Syed, and Mark Finley of Omnipoint Communications, Inc. (Omnipoint) for a field review on this petition in the Town of Woodbridge, Connecticut.  Omnipoint is petitioning the Council for a determination that no Certificate of Environmental Compatibility and Public Need is required for proposed modification to a Connecticut Light and Power Company (CL&P) electric transmission line support structure in Woodbridge.

Omnipoint submits no Certificate would be required because the addition of a proposed antenna and associated equipment by Omnipoint would not have a substantial adverse environmental effect.

Omnipoint proposes to attach an antenna to the top of existing 81-foot CL&P transmission line tower structure number 2384 off Johnson Road at the Oak Lane Country Club (Country Club) Association.  Access would be from Johnson Road through the Country Club on an access road used by the Country Club to service a golf course.  A temporary staging area would be established adjacent to structure number 2384.  A PCS antenna would be placed on top of the CL&P structure, with the top of the antenna being approximately 91 feet above ground level.  The proposed antenna is approximately 60 inches in height, 7 inches in diameter, and weighs 27 lbs.  Communications equipment would be placed on a new 10-foot by 5.5-foot concrete slab installed near the base of the tower.  Existing vegetation around the base of the tower would serve to screen the equipment building.  The total calculated radio frequency power density at the base of the tower would be 0.035 mW/cm2, which is 3.5 percent of the maximum permissible exposure for uncontrolled environments based on Federal Communications Bulletin 65, August 1997.