Petition No. 405

Omnipoint Communications, Inc.

Stratford, Connecticut

Staff Report

December 17, 1998

On December 15, 1998, Connecticut Siting Council (Council) Executive Director, Joel M. Rinebold, Council member Brian Emerick and Robert Erling of the Council staff met J. Brendon Sharkey, Haider Syed, and Mark Finley of Omnipoint Communications, Inc. (Omnipoint) for a field review on this petition in the Town of Stratford, Connecticut.  Omnipoint is petitioning the Council for a determination that no Certificate of Environmental Compatibility and Public Need is required for proposed modification to a Connecticut Light and Power Company (CL&P) electric transmission line support structure in Stratford.

Omnipoint submits no Certificate would be required because the addition of a proposed antenna and associated equipment by Omnipoint would not have a substantial adverse environmental effect.

Omnipoint proposes to attach an antenna to the top of the existing 101-foot CL&P transmission line tower structure number 1321 off Chapel Road.  Access would be directly from Chapel Road to the existing CL&P right-of-way now used by CL&P to service transmission lines and structure number 1321.  A temporary staging area would be established adjacent to this structure in the CL&P right-of-way.  A PCS antenna would be placed on top of the CL&P structure, with the top of the antenna being approximately 109 feet, eight inches above ground level.  The proposed antenna is approximately 56 inches in height, 2.75 inches in diameter and weighs 18 lbs.  Communications equipment would be placed on a new 10-foot by 5.5 foot concrete slab installed near the base of the tower.  Town records indicate this site is not within an inland wetland.  The total calculated radio frequency power density at the base of the tower would be 0.0112 mW/cm2, which is 1.12 percent of the maximum permissible exposure of uncontrolled environments based on Federal Communications Bulletin 65, August 1997.